## Slide 1: OpenFlow-based Distributed NAT
Team4(Shawn, chrysan,sANTA)
2016/1/22 @SHENZHEN odl-hACKSON

## Slide 2: Problem Statement
Why Egress NAT
  IPv4 address is exhausting
  More & more VMs are coming up
  Public IP addresses become most expensive resource
  In public cloud environment IP address is shared
GW/NAT
Switch
Switch
Switch
Switch
Host
Host
Host
Host
Host
Host
Host
Host
6.6.6.6:3080<->10.0.0.2:2120
6.6.6.6:3090<->10.0.0.3:2130
…. ….
10.0.0.2
10.0.0.3
10.0.0.4
Internet
Traditional Egress NAT
  Public IP & temporary port for each flow
  Deployed in GW device
  Single point of failure

## Slide 3: Our Solution
Distributed NAT
  Separated data plane and control plane
  NAT forwarding function distributed in each TOR with OpenFlow (e.g.: change packet header & forward)
  NAT control logic center on ODL based SDN Application (e.g: assign & maintain IP & port mapping)
  Performance & Scale
  No single point of failure
OF Switch
OF Switch
OF Switch
OF Switch
Share Public IP: 6.6.6.6
10.0.0.2
10.0.0.3
10.0.0.4
Internet
ODL
GW
Distributed NAT
APP
NAT
NAT
NAT
NAT

## Slide 4: System Architecture
OF Switch
OF Switch
NAT Logic
OF Handler Rest Server
RESTCONF API
Of-Plugin
External APP
ODL
Packet-in / Flow-removed events
Packet-in/packet-out/flow-mod
MD-SAL
Internal
APP
Mapping
DB
  Application Type: Hybrid (External & Internal)
  Internal APP (MD-SAL):
    Subscribe to MD-SAL for Packet-in & flow-removed events
    Send OF packets to external app for further processing
  External App (RESTCONF)
    Receive flow info from Internal APP
    Do NAT logic (assign IP & dynamic port, maintain mapping)
    Call ODL RESTCONF API to add Flow
  OpenFlow Rules
    SNAT: Match: ethernet-match, ipv4-source, ip-match, tcp-source-port; Action: set nw-src, set tp-src, ouput
    DNAT: ethernet-match, ipv4-destination, ip-match, tcp-destination-port; Action: set nw-dst, set tp-dst, output
Topology DataStore

## Slide 5: Walk through
1. Set up network topology: mininet, odl controller, l2switch learn top
2. Initialize flow rules (Proactive): fix demonstration net problem
3. Internal app register & listen to MD-SAL, subscribe to openflow packet-in & flow-delete events
3. Reactive NAT flow: 1) h1 ssh h3; 2) s1 packet in to ODL; 3) internal app get notification, parse packet, pass src-ip, dst-ip, src-port, dst-port, ofswitch interface information to external app; 4) external app get invoked, do NAT logic, assign public ip & src-port if needed, and maintain mapping; 5) prepare add_flow data, call ODL Restconf API to add flow to switches
4. OpenFlow ruels:
  sNat (on s1/s2): Match 6 tuple (ip, srcip, tcp, srcport), action: set-nw-src & set-tp-src
  dNat(on s1/s2): Match 6 tuple (ip, dstip, tcp, dstport), action: set-nw-dst & set-tp-dst
  Forward (s3): Match 6 tuple (ip, srcip, dstip, tcp, srcport, dstport), action: output
OF Switch
s1
Host h1
OF Switch
s3
OF Switch
s2
Host h2
Host h3
10.0.0.2/32
10.0.0.3/32
10.0.0.4/32 (fake as public address)
internet
intranet
ODL
2. Packet in
3.Flow_mod
1. Send packet

## Slide 6: Status & Next
Where we are?
Internal APP: Done (able to get OF notification from MD-SAL, and send message to external app)
External APP: Basically done (able to get OF information from internal app, assign ip & port, maintain mapping, generate correct flow, add flow to switches through ODL RESTCONF API
What next?
Proactive flow consideration & design for NAT network
Protocols support: currently only tcp is supported, we will try extend to UDP/ICMP/ARP…
Internal APP: could be a common service in ODL, e.g. use message bus to send md-sal notification to external app
Contribute to ODL: Sample app commit; TcpPacket/UdpPacket processor (to get transport protocol port); api documents…

## Slide 7: Thank you!